## Slide 1
Cooperative Adaptive Cruise Control
Team 3
Ishita Pal - 5G Transmitter
Neethu Jose - 5G Receiver
Sung-Lin Chen – Radar Receiver
Yi-Chien Chiang – Radar Transmitter

## Slide 2: System Overview
ACC (Adaptive Cruise Control)
  Allows vehicles to speed up and slow down automatically in order to keep pace with the traffic ahead using radar
  Breakthrough technology in vehicle safety system
  In 1995, Mitsubishi was the first OEM to offer ACC in their Diamante sedan
CACC (Cooperative Adaptive Cruise Control)
  Evolution of ACC
  Using 5G to achieve vehicle-to-vehicle (V2V) communication
  CACC equipped vehicle can interact with more vehicles and surrounding environment

## Slide 3: System block diagram
Vehicle
Radar Control System
Radar Transceiver
Target Vehicle In Front
5G communication link
V2V - 5G
Radar
Host vehicle
Preceding vehicle

## Slide 4: Top Level Specs
5G Comm.
- Frequency (15GHz)
- Range ( ~ 1000m)
- Antenna Tx and Rx (Horn Antenna)
ACC Radar
- Frequency (77GHz)
- Range ( ~ 80m)
- Antenna Tx and Rx (E-Band Lens Array Antenna )

## Slide 5: Transmitter and Receiver Block Diagram- Radar
LPF
LPF
IF
Mixer
BPF
PA
Antenna
BPF
Mixer
IF
Oscillator
LNA
DA
FIF =1 GHz
FLO =76 GHz
FLO =76 GHz
FRF =77 GHz
FIF =1 GHz
BPF
LNA

## Slide 6: Radar Transmitter
IFin = 1GHz
LO = 76GHz
FRF = 77GHz

## Slide 7: Radar TX Calculation
Pin = 15dBm = 31.62mW
Pout = 28.04dBm = 636.76mW
Pdc = 1500mw + 6750mw + 4125mw = 12375mW
PAE(%) = 4.9%
Gt = 20dBi
EIRP = Pt + Gt = 28.04dBm + 20dBi = 48.04dBm
MDS = N = KTB = -113.86dBm = 4.1*10-9 mW
fo = 77GHz
𝜎 = 1m2
𝜆 = 0.0392m
= = 76.8m
FSPL = = 107.87dB

## Slide 8: Radar TX Gain and Node Power

## Slide 9: Radar TX Gain and Node Power Yield Simulation

## Slide 10: Low Pass Filter -LPF1R25-22R5-SFF
Parameter | Value
Model | LPF1R25-22R5-SFF
Frequency Range | 0 –1.25 GHz
Insertion Loss | 1-1.5 dB
MIXER - SFQ-75311415-1010SF-N1-M
Parameter | Min. | Typ. | Max.
RF Frequency | 75GHz |  | 108GHz
LO Frequency | 75GHz |  | 108GHz
IF Frequency | 0GHz |  | 20GHz
LO Power |  | 15dBm | 20dBm
Conversion Loss |  | 15dB | 

## Slide 11: Local Oscillator - SOM-77302315-12-M1
Parameter | Value
Model | SOM-77302315-12-M1
Frequency Range | 75.5GHz – 77.5GHz
Power Output | 15dBm
Bias Voltage | +5.5 VDC
Bias Current | 750 mA
Operating Temperature | 0 - 50˚C
BandPass Filter - SWF-77303350-12-B1
Parameter | Min. | Typ. | Max.
Passband Frequency | 75GHz |  | 78GHz
Passband Insertion Loss |  | 1.5dB | 
Passband Ripple |  | ±0.3 dB | 
Operating Temperature | -40˚C |  | +85˚C

## Slide 12: Driver Amplifier - AMP-12-02310
Parameter | Value
Model | AMP-12-02310
Frequency Range | 75 – 87 GHz
Gain | 16-21 dB
P1dB | 12dBm
PDC | 1.5 W
Power Amplifier - FPA-12-0001
Parameter | Value
Model | FPA-12-0001
Frequency Range | 71 – 77 GHz
Gain | 16 dB
P1dB | 28.5dBm
PDC | 6.75W

## Slide 13: Radar Receiver
RF Frequency: 77GHZ
Received Power: -39.83dBm
LO Frequency: 76GHz
IF Frequency: 1 GHz

## Slide 14: Radar RX Calculation
=77GHz ; ; ;
= = 107.87dB

## Slide 15: Radar RX Nominal

## Slide 16: Radar RX Yield Analysis: Gain

## Slide 17: Radar RX Yield Analysis: Noise Figure

## Slide 18: Radar RX Yield Analysis: IP3

## Slide 19: Antenna - ELA100.A
Parameter | Value
Frequency Range | 77GHz
Gain | 20dB
Beamwidth | 20°
Bandwidth | 1GHz

## Slide 20
Parameter | Min. | Typ. | Max.
Passband Frequency | 75GHz |  | 78GHz
Passband Insertion Loss |  | 1.5dB | 
Passband Ripple |  | ±0.3 dB | 
Operating Temperature | -40˚C |  | +85˚C
BandPass Filter - SWF-77303350-12-B1
Low Noise Amplifier 1: CHA2080-98F
Parameter | Value
Manufacture | United Monolithic Semiconductors
Model | CHA2080-98F
Frequency Range | 71 – 86 GHz
Gain | 22 dB
P1dB | 10dBm
Noise Figure | 3.5dB
PDC | 262.5mW

## Slide 21: Local Oscillator - SOM-77302315-12-M1
Parameter | Value
Model | SOM-77302315-12-M1
Frequency Range | 75.5GHz – 77.5GHz
Power Output | 15dBm
Bias Voltage | +5.5 VDC
Bias Current | 750 mA
Operating Temperature | 0 - 50˚C
MIXER - SFQ-75311415-1010SF-N1-M
Parameter | Min. | Typ. | Max.
RF Frequency | 75GHz |  | 108GHz
LO Frequency | 75GHz |  | 108GHz
IF Frequency | 0GHz |  | 20GHz
LO Power |  | 15dBm | 20dBm
Conversion Loss |  | 15dB | 

## Slide 22: Low Pass Filter -LPF1R25-22R5-SFF
Parameter | Value
Model | LPF1R25-22R5-SFF
Frequency Range | 0 –1.25 GHz
Insertion Loss | 1-1.5 dB
Low Noise Amplifier 2: ABX/00102-1530
Parameter | Value
Manufacturer | CTT Inc.
Model | ABX/00102-1530
Frequency Range | 0.1GHz-20GHz
Gain | 30dB
P1dB | 10dBm
Noise Figure | 1.5dB
PDC | 1600mW

## Slide 23: Transmitter and Receiver Block Diagram- 5G
Transmitter Block Diagram
Receiver Block Diagram
IF INPUT
Mixer
BPF
LNA
LO
PA
PA
Antenna
Mixer
IFA
LO
Antenna
IFA
BPF
LPF
LNA
IF output
FRF =15 GHz
FLO =14 GHz
FIF =1 GHz
FRF =15 GHz
FIF =1 GHz
FLO =14 GHz

## Slide 24: 5G Communication Transmitter
IF Freq= 1 GHz
LO Freq = 14 GHz
RF Freq = 15 GHz

## Slide 25: 5G Comm. TX - Cascaded Gain Graph
Nominal Cascaded Gain (G) = 46.44 dB

## Slide 26: 5g comm. Tx – cascaded node power
Nominal Cascaded Power (Pt) = 36.44 dBm

## Slide 27: 5G TX Calculation
Pin = -10 dBm = 0.1 mW
Pout = 36.44dBm = 4415.70 mW
Pdc = (5*65)+(6*210)+(24*240) = 7345 mW
PAEtotal = (Pout - Pin)*100/ Pdc = 60.11%
Pt = 36.44 dBmW = 6.44 dBW = 4.405W
Gt = Gr = 20 dB = 100
EIRP = Pt + Gt = 56.44 dBm = 26.44 dB = 440.55W
f = 15 GHz λ = c/f = 0.02
Pr = -39.5 dBmW = -69.5 dBW= 112.2 nW
R = √( Pt *Gt* Gt* λ2 )/( Pr *(4*π)2) = 999.59 m

## Slide 28: LNA - QPL9547
Parameters | Values
Frequency | 0.1-6 GHz
Gain | 19.5 dB
OIP3 | 39 dBm
P1dB | 22.7 dBm
Noise Figure | 0.3 dB
Current | 65 mA
Supply Voltage | 5 V

## Slide 29: Mixer - MAMX-011067
Parameter | Units | Min. | Typ. | Max.
LO and RF Frequency | GHz | 5 |  | 20
IF Frequency | GHz | 0 |  | 6
LO Power | dBm |  | 15 | 
Conversion Loss | dB |  | 7 | 9
Input P1dB | dBm |  | 8 | 
Input IP3 | dBm |  | 18 | 
Local oscillator - VTO-13500-22M

## Slide 30: Bandpass filter - BPF13751625-S_A
Parameters | Values
Frequency | 13.75-16.25 GHz
Impedance | 50 Ω
Center Frequency | 15 GHz
Insertion loss | 1 dB
Ripple | 1 dB
Return Loss | 14 dB

## Slide 31: Power amplifier 1 TGA2565-SM
Parameters | Values
Frequency | 11- 17 GHz
Gain | 27 dB
OIP3 | 34 dBm
P1dB | 27 dBm
Psat | 28.2 dBm
Current | 210 mA
Supply Voltage | 6 V
Noise Figure | 5.5 dB
Power amplifier APN226
Parameters | Values
Frequency | 13.5-15.5 GHz
Gain | 20 dB
Psat | 39.5 dBm
P1dB | 36.5 dBm
Output Return loss | 12 dB
Current | 240 mA
Supply Voltage | 24 V
GaN Power Amplifier

## Slide 32: Antenna - pe9854/sf-20

## Slide 33
5G Communication Receiver
FIF =1 GHz
FLO =14 GHz
FRF =15 GHz
Pr =-39.5 dBm

## Slide 34
5G Receive Channel Simulation
Cascaded NF = 1.66 dB
Cascaded Gain = 43.17 dB
Cascaded IP3= 36.19 dBm

## Slide 35
YIELD analysis- IP3 & NF

## Slide 36
YIELD analysis- GAIN

## Slide 37: LNA - CMD157
Parameter | Value
Manufacturer | Custom MMIC
Model | CMD157
Frequency Range | 6-18 GHz
Gain | 26 GHz
Noise Figure | 1.5 dB
Output P1dB | 11 dBm
OIP3 | 22 dBm

## Slide 38: Lowpass filter - LP0805H1250ASTR
Parameter | Value
Manufacturer | AVX RF
Model | LP0805H1250ASTR
Frequency Range | 0 –1.25 GHz
Insertion Loss | 0.7 dB
IMAGE Reject filter - B0315G12
Parameter | Value
Manufacturer | Microwave Circuits
Model | B0315G12
Passband Frequency Range | 14.88 - 15.38 GHz
Passband Insertion Loss | < 1.8 dB
Bandwidth @ 3dB | 400 MHz

## Slide 39: Mixer & LO
Parameter | Value
Manufacturer | Pasternack
Model | PE86X1009
LO and RF Frequency | 7-43 GHz
IF Frequency | 0-10 GHz
LO Power | 13 dBm
Conversion Loss | 9 dB
Parameter | Value
Manufacturer | Microwave Dynamics
Model | DRO-1000
Frequency | 1-50 GHz
LO Power | 13 dBm
DC Power | 10V*90mA = 0.9W

## Slide 40: IF Amplifier - TQL9048
Parameter | Value
Manufacturer | TriQuint
Model | TQL9048
Frequency Range | 0.05 -4 GHz
Gain | 14.5 GHz
Noise Figure | 1.7 dB
Output P1dB | 22 dBm
OIP3 | 40.5 dBm

## Slide 41: 5g Receiver Calculation
Pt = 36.46 dBmW
Gt = 20dB
f = 15 GHz
λ = c/f = 0.02
FSPL = (4*π*R)2 / λ2 =3.94 x 1011 → 115.96 dB
𝑃𝑟=𝑃𝑡+𝐺𝑡+𝐺𝑟−𝐹𝑆𝑃𝐿 = 36.46 + 20 + 20 - 115.96 = -39.5 dBm
𝑀𝐷𝑆=𝑁0=𝑘𝑇𝐵=𝑘 (151.85 𝐾)(1.25 G𝐻𝑧) → -85.817 dBm

## Slide 42: 5G Tx & Rx Channel

## Slide 43: 5G Tx & Rx Channel
FSPL= -115.96dB
Antenna Gain = 20 dB

## Slide 44: 5G Comm Link Spec Compliance Matrix
Parameter | Initial Spec | Reason for Changing Spec | Min/Max | Simulated Performance | Compliant (Y/N)
Frequency Band (GHz) | 14.5 - 15.5 |  | Min | 15 | Y
Transmit Output Power (dBm) | 33 |  | Min | 36.44 | Y
Transmit Channel Gain (dB) | 30 | To achieve Pt atleast 33 dbm | Min | 46.17 | Y
Transmit Channel PAE (%) | 50 |  | Min | 60.11 | Y
Receive Noise Figure (dB) | 2 |  | Max | 1.66 | Y
Receive Channel Gain (dB) | 25 | To achieve Pout nearly 0 dbm | Min | 46.44 | Y
Receiver Channel OIP3 (dBm) | 25 | To achieve Pout nearly 0 dbm | Min | 36.19 | Y
TX Antenna Az Beamwidth (degrees) | +/- 60 |  | Max | 24.5 | Y
RX Antenna Az Beamwidth (degrees) | +/- 60 |  | Max | 24.5 | Y
Range (m) | 1000 |  | Min | 999.59 | N
Total DC Power Consumption (W) | 5 | DC power consumption is larger than expected | Max | 7.72+2.35=10.07 | N

## Slide 45: Radar TX And RX Channel

## Slide 46: Radar TX And RX Graph

## Slide 47: Top-level Compliance Matrix: Radar
Parameter | Original Spec | Min/Max | Simulated Performance | Compliant (Y/N)
Frequency Band (GHz) | 76 – 77 | Min | (77) 76.5-77.5 | N
Transmit Output Power (dBm) | 33 | Min | 28.04 | N
Transmit Channel Gain (dB) | 27 | Min | 13.04 | N
Transmit Channel PAE (%) | 30 | Min | 4.9% | N
Receive Noise Figure (dB) | 3 | Max | 6.9 | N
Receive Channel Gain (dB) | 20 | Min | 40.78 | Y
Receiver Channel OIP3 (dBm) | 23 | Min | 20.38 | N
Antenna Beamwidth (degrees) | +/- 3 | Max | 20 | N
Range (m) with Target RCS=1.0m^2 | 100 | Min | 78.4 | N
Total DC Power Consumption (W) | 2.5 | Max | 12.37 +4.71=17.08 | N

## Slide 48: DC Power Calculation
DC source : Lead-Acid Battery from the Vehicle
𝑃𝐷𝐶,5G𝑅𝑋 = 𝑃𝐷𝐶,𝐿𝑁𝐴+2(𝑃𝐷𝐶,𝐼𝐹𝐴𝑚𝑝)+𝑃𝐷𝐶,𝐿𝑂 = (3V*52mA) + 2(5V*130mA) + (10V*90mA) = 2.35W
𝑃𝐷𝐶,5GTX = PDC,LNA + PDC,PA1+ PDC,PA2+ PDC,LO = (5V*65mA)+(6V*210mA)+(24V*240mA)+(5V*75mA) = 7.720W
𝑃𝐷𝐶,Radar𝑅𝑋 = 𝑃𝐷𝐶, LNA1+𝑃𝐷𝐶, LNA2 + 𝑃𝐷𝐶,𝐿𝑂 = 262.5mw + 1600mw + 4125mw =5.987W
𝑃𝐷𝐶,RadarTX = 𝑃𝐷𝐶, 𝐷𝐴+𝑃𝐷𝐶, P𝐴 + 𝑃𝐷𝐶,𝐿𝑂 = 1500mw + 6750mw + 4125mw =12.375W

## Slide 49: Environmental, Performance, & Consumer Issues
A CACC system may not work properly in certain weather conditions like heavy rain or fog where 5G signal can be severely interfere.
The gap between the CACC vehicle may be short enough to deter most cut-in lane changes in multi-lane highway environment.
Security attacks like manipulating speed limit, Denial of Service (DoS) attacks on the engine, unauthorized brake, and attacks on active brake function, threaten the safety of passengers.

## Slide 50: Meeting standards for Human Exposure for RF signal
Maximum power density for human exposure to RF and microwave electromagnetic fields is 10mW/cm2
For 5G
Power Density=(Pt* Gt)/(4π*D2)=10mW/cm2
D = [(4.425*100)/(4π*100)]0.5= 0.59m
For Radar
Power Density=(Pt* Gt)/(4πD2)=10mW/cm2
D = [(0.563*100)/(4π*100)] 0.5 =0.21 m
** We can provide a shield to reduce the human exposure to RF signals generated by the system.

## Slide 51: Manufacturing and Test issues
There isn’t one uniform system in place across all car makers and models, so drivers may need to learn a new car’s CACC system each time.
The improvement of traffic efficiency largely depends on the level of CACC deployment.
Testing for abnormal circumstances on the road, for instance, sudden car accident, goods dropped from front vehicle.

## Slide 52: Schedule
Task Name | Completion Date
DESIGN | 
Problem Description | September 2020
Top Level Specifications | November 2020
DEVELOPMENT | 
Prototype Design | January 2021
Prototype Construction | April 2021
Testing & Integration | June 2021
Debugging | September 2021
Final Testing | December 2021
PRODUCTION | 
Final Design Submission | July 2022
Complete Bill of Material | September 2022
Product Release | December 2022

## Slide 53: Summary
Cooperative Adaptive Cruise Control (CACC)
  Using 5G to achieve vehicle-to-vehicle (V2V) communication
  CACC equipped vehicle can interact with more vehicles and surrounding environment
  Helps in stability of traffic flow & safety of the drivers.

## Slide 54
V2V - 5G
Radar
Host vehicle
Preceding vehicle